## Slide 1: Delta Levees Investment Strategy CVFPB Briefing
July 22, 2016

## Slide 2: Today’s Discussion
Background and Purpose
Risk and Level of Protection
Risk Results
Prioritizing Approach
Next Steps
1
2
3
4
5
2

## Slide 3: 158 levee failures since 1900
Apparent declining rate of failure since the 1970s
3

## Slide 4: Sacramento-San Joaquin Delta Reform Act of 2009
  85305. (a) The Delta Plan…reduce risks to people, property, and state interests…by promoting…strategic levee investments.
  85306. The council, in consultation with the Central Valley Flood Protection Board, shall recommend…priorities for state investments in levee operation, maintenance, and improvements

## Slide 5: The assignment: Reduce risk in the Delta
People
Property
State Interests
  Coequal goals
    Water supply
    Ecosystem
  While considering the Delta as an evolving place

## Slide 6: The expected outcome: Delta Levees Investment Strategy
Priority islands and tracts for investment
Comprehensive risk reduction strategy
Delta Plan policy changes
Recommendations to the Legislature and other agencies

## Slide 7: Tolerable Risk vs. Level of Protection
7

## Slide 8: What is risk?
What is in harm’s way? How vulnerable is it?
What are the hazards and how likely are they to occur?
How will the structure perform?
Risk = Probability X Consequences

## Slide 9: If we want to prioritize where to spend money…
Highest risk
  High probability of occurrence
  High consequences
Cost-effective actions to reduce risks
  More bang for the buck
Manage residual risk
  What risk is tolerable?
Sacramento 1862

## Slide 10: Current Level of Protection approach is limited
Considers only the probability of occurrence
Ignores the adverse consequences of flooding
Focuses on structural actions
    Reduces focus on other actions to reduce risk
Implies that risk can be eliminated
    100-year (or 200-year) protection is “safe”

## Slide 11: One Percent Level of Protection
Delta Stewardship Council
Current Guidance
One percent AEP—NFIP (44CFR 65.10)
  “100-year” level-of-protection
  Basis for certification and FEMA accreditation
Limitations
On the land-side of levee
  No insurance is required
  No special mitigation is required

## Slide 12: Limitations of the Level of Protection approach
The one-percent annual chance LOP is not a safety standard
  Basically an insurance standard
  Focuses on the hazard
  Ignores consequences
  Implies risk can be eliminated
  Favors structural solutions
  Hard to measure
    Risk reduction
    Cost-effectiveness

## Slide 13
We make decisions everyday based on risk

## Slide 14: Principles of Tolerable Risk approach
Risk cannot be ignored
Absolute safety cannot be guaranteed
Life safety is paramount (USACE)
Risk should be As Low As Reasonably Practicable, or ALARP
ALARP is what can be reasonably done without spending an inordinate amount of time, money, or resources relative to the risk reduction benefits

## Slide 15
PROBABILITY
CONSEQUENCES
HIGH
LOW
HIGH
LOW
Plane Crash
Auto Accident
Dams
Mining Accident
LIMIT OF TOLERABLE RISK?
RISK = PROBABILITY x CONSEQUENCES
How Much Risk is Tolerable?
MORE TOLERABLE
LESS TOLERABLE

## Slide 16
Unacceptable
Broadly acceptable
Risk cannot be justified except under extraordinary circumstances
Range of Tolerability
No further actions required. Risk regarded as insignificant
Tolerable Risk

## Slide 17
PROBABILITY
CONSEQUENCES
HIGH
LOW
HIGH
LOW
CURRENT RISK
IMPROVE LEVEES
IMPROVE EVACUATION
LEVEES DETERIORATE
POPULATION GROWS
RISK = PROBABILITY x CONSEQUENCES
How Does Risk Change?

## Slide 18: Tolerable Risk Guidance
Best practices identified by USACE and USBR (2015)
USACE Design and Construction of Levees (2016) will encourage risk assessment procedures

## Slide 19: Applying the Tolerable Risk approach
Identify Options to Reduce Risk
Structural
  Non-structural
  Calculate risk reduction
Characterize Risk
  Inventory assets
  Identify hazards
  Assess vulnerabilities
  Calculate risk
Continuously Review
  Communicate risks
  Adapt to change
  Perform robust OMRR&R*
Evaluate Options
  Do measures reduce risk to tolerable levels?
  Compare cost-effectiveness and trade-offs
  Assess residual risk
1.
2.
3.
4.
*Operations, maintenance, repair, replacement, and rehabilitation
Initial DLIS priorities based on risks and opportunities

## Slide 20: Advantage of Tolerable Risk
If you can measure risk, you can measure the cost-effectiveness of efforts to reduce risk
Facilitates
  Understanding risk
  Communicating risk
  Managing risk
Recognizes
  Risk cannot be eliminated
  Absolute protection is not possible
Enables
  Evaluation of trade-offs and cost-effectiveness
  Efficient use of resources
  Establishing priorities
  Fair treatment
  Accounts for
  Both structural and non-structural options

## Slide 21: Applying tolerable risk Approach to the delta
21

## Slide 22: State Interests in the Delta

## Slide 23: Delta Assets
Lives
  Population
Property
  Property value (structures and crops)
  Infrastructure systems of statewide importance
Water Supply
  Islands important for water quality, conveyance, and water supply infrastructure
Ecosystem
  Terrestrial habitat and managed floodplains
  Tidal and riparian habitat
Other Delta as Place Considerations
  Legacy towns, prime agricultural lands, and public roadways

## Slide 24: Risk Metrics in the Delta
Expected Annual Damage (EAD)
Expected Annual Fatalities (EAF)
Harm to Delta as a place
Water Supply Disruption
Harm to the Ecosystem

## Slide 25: Delta Risk Maps
FLOOD DAMAGE RISK (EAD)
ECOSYSTEM RISK
LIFE LOSS RISK (EAF)
WATER SUPPLY RISK
RISK TO DELTA AS A PLACE

## Slide 26: Probability of Flooding

## Slide 27: Preliminary Delta Risk Maps – Lives & Property

## Slide 28: Risk to High-value Terrestrial Habitat

## Slide 29: Water Supply Disruption
By function
  Salinity barrier
  Conveyance corridor
  Infrastructure
  By user group
  10 major user groups
By percent of Delta diversions

## Slide 30: Additional Delta Information
Potential for Tidal Habitat
Islands with Legacy Towns

## Slide 31: Additional Delta Information
Prime Agricultural Lands
Islands with Public Roadways

## Slide 32: Example Tiered Risk Map
Example Composite Risk
  Expected Annual Fatalities
  Expected Annual Damages
  Risk of Water Supply Disruption
  Risk of Habitat Damage

## Slide 33: Tiered Risk Map, with tidal habitat potential

## Slide 34: Applying Tolerable Risk Guidelines in the Delta
Enables clear communication of risk to decision-makers, stakeholders and the public
Identifies areas of highest risk
Places appropriate focus on the risk to life safety
Enables using risk metrics to inform decisions and prioritize investments
  Lives and property
  Water supply
  Ecosystem
  Delta as a place
Provides an open and transparent basis for prioritizing investments
Image: Andrea Gaffney
34
July 19, 2016

## Slide 35: Next Steps – Near-term
Identify high priority islands for investment
Prepare draft risk reduction strategy
    Investment priorities
    Delta Plan risk reduction policy changes
    Delta Plan recommendations
Begin CEQA review
Prepare report to the Legislature
    Priorities and recommendations

## Slide 36: Next Steps – Long-term
Identify Options to Reduce Risk
Structural
  Non-structural
  Calculate risk reduction
Characterize Risk
  Inventory assets
  Identify hazards
  Assess vulnerabilities
  Calculate risk
Continuously Review
  Communicate risks
  Adapt to change
  Perform robust OMRR&R*
Evaluate Options
  Do measures reduce risk to tolerable levels?
  Compare cost-effectiveness and trade-offs
  Assess residual risk
1.
2.
3.
4.
*Operations, maintenance, repair, replacement, and rehabilitation

## Slide 37: dISCUSSION