## Slide 1: City of Sacramento, Department of Parks & Recreation Authorizing existing Baler Building July 26, 2019
APPLICATION NO. 19370

## Slide 2: BOARD ACTION
Consider approval of Permit No. 19370:
To authorize the single-story, 3,246 square foot, slab-on-grade structure; and
To authorize the perimeter fence is chain link and is 8 feet high.

## Slide 3: PROJECT MAP
The project is located at/under the Sacramento Bypass about 3 miles north of the City of West Sacramento, Yolo County.
Approximate Project Location

## Slide 4: PROJECT ANALYSIS
The City requests authorization of the existing Baler Building, which is currently used as a skate park, and a perimeter fence on the landside of the left (south) bank levee crest of the American River. The building was constructed by the City in 1991 for use as a trash transfer facility. Ground elevations on the landside of the levee are equal to or exceed the levee crown elevation;
Based on the levee cross-section prepared by the City, the foundations for both the building and fence posts are well above the design water surface elevation of the American River. Consequently, these features do not have a major detrimental impact to the levee which is discussed in the following sections. In addition, the location of the building and fence do not restrict access to the levee or interfere with levee maintenance.

## Slide 5: PROJECT DRAWINGS

## Slide 6: HYDRAULIC ANALYSIS
The Project is approximately 8.3 feet above the U.S. Army Corps of Engineers (USACE) design water surface elevation. Therefore, a hydraulic analysis was not required.

## Slide 7: GEOTECHNICAL ANALYSIS
As the building and fence are existing features, no geotechnical analysis was required. Additionally, the structure foundations are above the design water surface elevation which does not pose any levee safety issues.

## Slide 8: Project Waivers of Standard
The City has requested a waiver to Title 23, Section 113, b(6)(A) which requires that structures may not be constructed on a levee section or within ten (10) feet of a levee toe and Title 23, Section 126 (a)(B)(2) which requires that all fences parallel to a levee must be located a minimum distance of ten (10) feet off the levee toe.
Title 23, section 11 (d) states that where the Executive Officer (EO) finds in a particular situation that there is no legitimate reason for the application of one of the board’s standards, the EO may waive any such standard for that situation.

## Slide 9: Project Waivers of Standard
The structure and fence are located on the landside of the levee at the same elevation as the levee crown.
The structure and fence do not restrict access to the levee crown.
As the foundations for both structure and fence are above the design flood elevation of 38.01 feet, the structure and fence do not pose a threat to levee stability.
The structure and fence do not prevent levee maintenance as exemplified by the endorsement from the local maintaining agency, American River Flood Control District.
The waivers applies to this facility and will not apply to any future addenda without further consultation.

## Slide 10: AGENCY COMMENTS/ENDORSEMENTS
The American River Flood Control District (ARFCD) endorsed the application on March 20, 2017, with conditions. All applicable ARFCD conditions have been incorporated into the permit.
USACE 33 U.S.C. 408 approval letter has not yet been received for this application. Staff anticipates receipt of a letter indicating that the USACE Sacramento District Engineer approves the request to alter the Federal flood risk reduction project, subject to conditions. Staff will review the USACE letter to ensure its conformity with the permit language and incorporate it into the permit as Exhibit A.

## Slide 11: CEQA CONCLUSIONS
Staff has prepared a CEQA analysis, as included in the Staff Report. For information regarding staff’s CEQA analysis, refer to Section 8.0 of the Staff Report.

## Slide 12: 8610.5 CONSIDERATIONS
Staff has prepared the 8610.5 Considerations, as included in the Staff Report. For information regarding staff’s analysis, refer to Section 9.0 of the Staff Report.

## Slide 13: STAFF RECOMMENDATION
Adopt the CEQA Findings;
Staff recommends that the Board:
Approve Permit No. 19370; and
Direct the Executive Officer to take necessary action to prepare and execute the permit and related documents and file a Notice of Exemption with the State Clearinghouse.

## Slide 14: QUESTIONS
?
Presented by: Deb Biswas, Permitting Section
Design Review: Deb Biswas, Permitting Section
Environmental Review: Ruth Darling, Environmental Program Manager
Document Review: Gary W. Lemon, P.E., Permitting Section Chief
Michael C. Wright, P.E., Chief Engineer
Legal Review: Sarah Backus, Staff Counsel