## Slide 1: DWR Streamgage North American Vertical Datum of 1988 Update of October 2019 July 26, 2019
Mitch Russo, P.E.
Hydrology and Flood Operations Office, DWR

## Slide 2: Purpose
All CA DWR Gages on same Zero reference
Modeling Advantages
  River profiles – slope downstream
Most recent flood studies in NAVD88
Recent LiDAR – NAVD88
USACE studies
Only the numbers are changing!
  New Monitor and Flood Stage Values

## Slide 3: Efforts To Date
2006
Sac/San Joaquin Delta
44 Total Gages
  4 Official NWS Forecast Points
  40 Data Points
2016
Sacramento Region
  Lower Sacramento River
  Lower American River
  Lower Feather River
5 Total Locations
  4 Official NWS Forecast Points
  Sacramento Weir Operating Criteria

## Slide 4: 2019 Datum Change October 1, 2019
Sacramento and Feather Rivers
21 Total Gages
  12 Official NWS Forecast Points
  9 Data Points
Calculations:
NGVD29 – Correction Factor = NAVD88

## Slide 6: Gage Datum Conversion Schedule
Finalize Conversion Values, Primary Stakeholder List
Finalize All Technical Resources
Q1
2019
Q2
2019
Q3
2019
Finalize Material for Secondary Stakeholders, Coordinate with CDEC Staff
Refine approach, if needed, based on primary stakeholders responses
Outreach to Secondary Stakeholders
LAUNCH
Oct 1, 2019
Outreach to Primary Stakeholders

## Slide 7: 2019 Datum Change October 1, 2019
Sacramento River at Red Bluff Diversion Dam
Correction Factor: -2.6’
NGVD29 – Correction Factor = NAVD88
Monitor Stage: 250.0’ – (-2.6’) = 252.5’ *
Flood Stage: 253.0’ – (-2.6’) = 255.5’ *
* Monitor and Flood Stages are rounded to the nearest half foot due to forecast limitations.

## Slide 8
=
Only the numbers are changing!
Old Datum (USED)
97.1’
New Datum (NAVD88)
96.9’
February 25, 2016

## Slide 9: Only the numbers are changing!
Old Datum (USED)
177.5’
New Datum (NAVD88)
177.4’
=
January 21, 2010

## Slide 10
2/11/2017 ~1500 hrs
Old Datum (NGVD29)
11.85’
New Datum (NAVD88)
4855.45’
=
Only the numbers are changing!

## Slide 11: NWS Actions Prior to October 1, 2019
Update E-19s and Internal Documentation
Translate Impacts to new NAVD88 datum values
Staff Training
Social Media notices – Public Outreach
CNRFC model and calibration modifications

## Slide 12: DWR Actions Prior to October 1, 2019
Move staff gages to reflect NAVD 88
Reset DCP’s to report data in NAVD 88
CDEC staff to apply temporary shift
  Temporary shift will be removed on Oct 1
Provide information to attendees of Pre-season Flood Outreach meetings

## Slide 13: Local Agency Impacts
Flood Hazard Plan/Annex?
Operating procedures?
Staff Training?
County Webpages?
Public Outreach?
Etc?

## Slide 14: Contacts
DWR
Boone Lek Boone.Lek@water.ca.gov
Mitch Russo Mitchel.Russo@water.ca.gov
NWS
Cindy Matthews Cindy.Matthews@noaa.gov
Tim Bardsley Tim.Bardsley@noaa.gov