## Slide 1: Sutter Bypass Two-Dimensional (2D) Hydraulic Model
Informational Briefing
Presented By Board Staff and CH2MHill Consultants
Model Funded by CVFPB, DWR, USF&WS
March 22, 2013

## Slide 2: Key Points to Discuss
Board Resolutions in 2008 and 2009 established initial goals
  Analysis of carrying capacity of the “1957 design flow”
  What capacity existed in 1950’s?
  What capacity exists today?
  Impact of the Sutter National Wildlife Refuge (SNWR) on capacity
Model type, geographic extent, boundary conditions
Development, calibration and verification
Initial conveyance and freeboard results for “1957 design” flows
How has available freeboard at 1957 flows changed since the 1950s?
Sensitivity runs demonstrate capabilities for CVFPP Regional and Basinwide planning analyses
Final reviews to publish a User Manual, Final Report, and Technical Memo
Turnover to DWR FloodSAFE Library of Models

## Slide 3: Board Directions / Model Objectives
Resolution 2008-19:
  Work with DWR and USACE to develop model to ascertain impacts of vegetation and structures on carrying capacity
  Confer with DWR and USACE to determine applicable design flows
Resolution 2009-11:
  Coordinate with DWR, USACE and USFWS to assess effect of SNWR on carrying capacity
  Determine if stated goals of flood management and stakeholder interests are achievable in the Bypass
    How does vegetation impact capacity?
    Do bridges and other structures impact capacity?
    Are there areas of compromised flood protection? If so what?

## Slide 4: Project Development / Study Area
Hired CH2M HILL consultants
  Assisted by MBK Engineers
  Peer reviewed by David Ford Engineers
Use RMA2 2D model (USACE)
Calibrated to 2006 event
Verified against 1997 event
Evaluate capacity for a range of design conditions
  1957 design profile
  O&M manual flows
  100-year event
  200-year event
Conduct sensitivity runs to determine capabilities to evaluate a variety of potential management practices and remedial measures
Feather River
Sutter Buttes
Yuba City
YOLO BYPASS
SR 20 Bridge
LOWER LIMITS
Sacramento River at Fremont Weir

## Slide 5: Model Details (CH2M)
Surface represented by a grid
  Over 43,000 elements
  Average size 1/2 acre (about 150 x 150 square feet)
Each element assigned unique characteristics
  Ground cover/land use (assigned to unique friction “n” values)
  Current elevation data based on 2010-11 CVFED LiDAR surveys (accuracy of +/- 0.3 feet)
Can modify element characteristics to evaluate change in land use, vegetation type, elevation, etc.

## Slide 6: RMA2 Model Answers Complex Questions (1/3)
  Allows us to simulate impacts of vegetation, land forms and structures in considerable detail

## Slide 7: RMA2 Model Answers Complex Questions (2/3)
Allows us to simulate impacts of vegetation, land forms and structures in considerable detail
Model resolution allows assignment of site-specific features to determine localized impacts

## Slide 8: The Model Provides an Important Tool
  Once delivered to DWR’s FloodSAFE Library of Models, it will provide a common platform to support the Basin-wide and Regional planning studies for the 2017 CVFPP update
  Assess impacts of potential management actions including changes in land use, vegetation type and pattern, sediment removal, structural changes, etc.
    Assess impacts of future maintenance practices
    Determine if existing top of levee profiles are sufficient to achieve current and future design standards

## Slide 9: Flow Comparison

## Slide 10: West Levee Freeboard Profiles (1957 design flow)
SNWR
(2010 land use)

## Slide 11: East Levee Freeboard Profiles (1957 design flow)
SNWR
(2010 land use)

## Slide 12: Areas of Freeboard < 5 feet with 1957 flows and 1950’s Top of Levee (design) profiles

## Slide 13: Areas of Freeboard < 5 feet with 1957 flows and 2007 Top of Levee (DWR Survey) profile

## Slide 14: Areas of Freeboard < 6 feet with 1957 flows and 1950’s Top of Levee (design) profiles

## Slide 15: Areas of Freeboard < 6 feet with 1957 flows and 2007 Top of Levee (DWR Survey) profile

## Slide 16: Multiple Sensitivity Runs Conducted
Three Initial Vegetation Scenarios
  2006 vegetation (baseline)
  2010-11 vegetation after thinning of 25 acres in the SNWR (existing conditions)
  Fully vegetated condition (120 % of baseline “n” values)
  A range of conditions representing various maintenance and management activities were simulated to determine model capabilities

## Slide 17: Sensitivity Run - Extensive Vegetation Management
3.2 feet max. reduction in WSEL.
SNWR
(2006 Land Use) with Vegetation Management

## Slide 18: Sensitivity Run - Moderate Vegetation Management
0.75 feet max reduction in WSEL
SNWR
(2010 Land Use) with Vegetation Management

## Slide 19: Sensitivity of Moderate Sediment Removal
0.19 feet max reduction in WSEL.
SNWR
(2010 Land Use) with Sediment Removal
(2010 Land Use) with Sediment Removal

## Slide 20: Conversion of SNWR to Ag use
SNWR
1.5 feet max reduction in WSEL.

## Slide 21: Summary and Next Steps
A robust model has been developed
Capable of evaluating changes in land use, vegetation type, sediment removal, levee and channel alignment, location and size of structures
Model results indicate that flows equivalent to the 1957 design WSEL can be conveyed by the Bypass without overtopping, but with less than the original design target of 5 to 6 feet of freeboard
Board staff will deliver the model and a final report, technical memo, and user guide to DWR’s FloodSAFE Library of Models for use by agencies, organizations and consultants
Board staff will also make documentation available on our website
Model will support the Basin wide and Regional flood planning processes to support the 2017 Central Valley Flood Protection Plan update
Board staff will inform Bypass landowners regarding the Board’s existing flowage easements

## Slide 22: Questions & Discussion
Electronic copies of the Report and User Guide will soon be available via our website
Board Staff
Dr. Sungho Lee, Engineer, Water Resources
(916) 574-2384, sungho.lee@water.ca.gov
David Williams, PE, Project Section Chief
(916) 574-2379, david.r.williams@water.ca.gov
Eric Butler, PE, Projects and Environmental Branch Chief
(916) 574-0707, eric.butler@water.ca.gov
CH2M Hill
Mark Glidden, PE
(720) 286-5135, mark.glidden@ch2m.com