## Slide 1: Hydraulic Screening and Analysis Needed for USACE Review
Greg Kukas, P.E.
Chief, Hydrology and Hydraulics Branch
U.S. Army Corps of Engineers (USACE), Sacramento District
July 25, 2014

## Slide 2: Overview
USACE role
Encroachment permit review process
  Hydraulic analysis review
  Risk impact assessment
  Thresholds used
  Screening-level analysis approach
  Additional analysis requirements
Concerns and challenges

## Slide 3: USACE Role
Why does USACE review CVFPB permits?
  As a requirement of:
    Project Partnership Agreements & O&M manuals
    33 USC 408
    33 CFR 208.10
  To assure ongoing performance of a federal project – i.e. acceptable flood risk impacts of proposed ‘encroachments’

## Slide 4: Encroachment Review Process
How does USACE fulfill its role?
  Geotechnical engineering review – assures the integrity of effected levees
  Assess flood risk impacts of the encroachment
    Hydraulic analysis review: verify the hydraulic changes expected to result from an encroachment
    Flood risk impact assessment: evaluate the acceptability of those changes from flood risk perspective

## Slide 5: Hydraulic Analysis Review
Fundamental concerns:
  Representative flow condition considered?
  Appropriate modeling tool and approach applied for the encroachment scenario?
  Sufficient detail used?
  Results accurate?

## Slide 6: Hydraulic Analysis Review
Representative flow conditions:
  Required:
    Original 1955/57 project design flows or
    O&M Manual specified flow
  Supplemental:
    Published 1/100 and/or 1/200 annual chance exceedance flows (i.e. “100-yr” or “200-yr” floods)
      USACE hydrology study
      FEMA base flood

## Slide 7: Hydraulic Analysis Review
Standard hydraulic modeling procedures:
  Select appropriate, relatively current model*
    Multiple sources: Corps, DWR, Consultants
    Multiple platforms: HEC-RAS, RMA2, FLO-2D, TuFlow
    Multiple versions accepted
  Refine model in vicinity of the proposed encroachment represent current condition
  Revise model to reflect ‘encroached’ conditions
    Physical obstructions: geometry changes
    Vegetative conditions: roughness coefficients
    Operational assumptions: debris loading
  Compare results
* - Key assumption: current conditions used as a baseline

## Slide 8: Hydraulic Analysis Review
Key hydraulic results:
  Water surface elevations (i.e. flood stages)
  Flow velocities and shear stress (relates to erosive force)
  At locations of maximum increase
    Usually located just upstream of the project
    Diminish in upstream direction
  Adjacent to levees or floodwalls
Notes: Highway traffic analogy

## Slide 9: Flood Risk Impact Assessment
How do hydraulic changes effect flood risk in the federal/state system?
  Risk = probability x consequences
  Flooding probability factors:
    Hydrology & hydraulics – frequency of flows with flooding potential
    Levee performance – factors: slope/stability, seepage, erosion, maintenance, flood fighting, visibility, etc.
  Flooding consequence factors:
    Population & damageable property
    Critical infrastructure and egress routes
    Floodplain depths & warning times
  Available freeboard
  Answer: it varies depending on setting-specific factors
Notes: Models available to more completely assess flood risk are cost-prohibitive and have their own limits.
USACE risk analysis requirement imposed on Section 408 permit situations is not applied.

## Slide 10: Flood Risk Impact Assessment
How do we assess how hydraulic changes affect flood risk associated with the federal/state system?
  Recognize the reliability of computed hydraulic effects
  Treat all settings as equal
  Apply professional judgment
  Adopt a prudent threshold criteria to account for the uncertainties and simplifying assumptions involved
  Assume negligible increase in flood risk if maximum increase in flood stage < 0.1’

## Slide 11: Flood Risk Impact Assessment
Why does USACE use 0.1’ as its acceptance threshold?
  It’s significantly less than the levee freeboard values incorporated into the design of the system
  It mitigates the potential for significant cumulative effects
  It’s comparable to the effects of the natural and dynamic characteristics of our system
  Because greater flood stage increases may be determined acceptable on a case by case basis with additional analysis and/or evaluation

## Slide 12: Screening-level Analysis
Simplified approach developed by USACE:
  For physical obstructions, if blocked area is < 1% of total cross-sectional area:
    Negligible flood risk increase is assumed
    No hydraulic analysis is required
  Supported by USACE-conducted hydraulic analysis
  Allows most truly minor encroachments to pass a “common sense”-type test with little less effort

## Slide 13: Additional Analysis Requirements
Detailed in USACE July 21, 2014 letter to CVFPB
  Closely coordinated with CVFPB staff
  Formalizes screening process and criteria
  Establishes 30-day window for USACE to request additional info
  Specifies debris loading assumptions for vertical blockage elements (e.g. bridge and dock piers)

## Slide 14: Additional Analysis Requirements
Debris loading assumptions:

## Slide 15: Concerns & Challenges
Cumulative impacts
When additional info needed
Borderline results:
  slightly > 1% blockage
  slightly > 0.1’ stage increase
Unique physical situations
Staff turnover and other resourcing demands
Constrained funding
Notes: DWR-developed library of models concept.